## Slide 1: The Hitchhiker’s Guide to Successful Residential Sensing Deployments
Timothy W. Hnat, Vijay Shrinivasan, Jiakang Lu, Tamim I. Sookoor, Raymond Dawson, John Stankovic, and
Kamin Whitehouse

## Slide 2: Sensing in Homes
Medical
Monitoring
Home
Automation
Energy
Management
People spend 65% of time in their homes
Notes: Today, people are increasingly deploying sensors in homes for a wide range of applications, including medical monitoring, home automation, and energy management.
People spend 65% of their time in their own homes (click), so these types of residential sensing applications have the potential for real impact on people’s daily lives and well being.

## Slide 3: Sensing in Homes
Extreme Environments
Indoors is hard too!
Photo courtesy of: Jan Beutel
Notes: Many researchers at this conference have gone to great lengths to deploy sensors in remote, extreme environments.
Today, we’re here to say that -- sensing indoors is hard too! (click)
… but maybe not in the same way  In fact, deploying a small number of sensors is very easy: plug them in, and wireless transmit data to a laptop.
At large scale, however, things become much more difficult.

## Slide 4: Sensing in Homes
1200 sensors
Over 20 homes
Up to 1 year/home
Difficulty
#Sensors
#Sensors < #Outlets
#Sensors > #Outlets
Notes: Over the past several years, our group has deployed over 1200 sensors in over 20 homes, sometimes for over a year at a time.
In the process of scaling up these deployments, we sometimes encountered a “phase transition”: (click) the difficulty of deployment increased discontinuously as we scale up
For example, (click) powering a small number of sensors is fairly easy: just plug them in to the wall. However, this suddenly becomes much more difficult when the number of sensors begins to exceed the number of power outlets in a house, which is typically only 30-40.

## Slide 5: Sensing in Homes
1200 sensors
Over 20 homes
Up to 1 year/home
Difficulty
#Sensors
#Homes < #Researchers
#Homes > #Researchers
#Homes
Notes: Similarly, deployment is fairly easy when researchers deploy in their own homes.
However, as the number of homes required for a study increases beyond the number of researchers, volunteers must be used. This suddenly makes a home more like the “remote environments” seen in some outdoor deployments, where researchers have very limited access for deployment and maintenance.

## Slide 6: Sensing in Homes
1200 sensors
Over 20 homes
Up to 1 year/home
Difficulty
#Sensors
#Days < ~1 month
#Days > ~1 month
#Homes
#Days
Notes: Finally, deployment suddenly become much more difficult over long time periods, and this is NOT just because sensors are more likely to fail: *people* become much less tolerant of annoyances and inconveniences from sensing experiments. Over long time periods of several months to a year, volunteers are no longer willing to help collect ground truth, tolerate wires and exposed circuit boards, or make time for frequent visits from researchers.

## Slide 7: Outline
Deployment Overview
Reliability and Failure Analysis
A Hitchhiker’s Guide
Notes: Before presenting the Hitchhiker’s Guide, (pause) we will give an overview of the deployments that we performed (pause) and present an analysis of failures we experienced during these deployments.

## Slide 8: Deployments Overview
Notes: `Our deployments include a wide range of sensing platforms, including both off-the-shelf products and custom systems that we designed and built.
We deployed:
1) Motion
2)Temp
Plugload
Power meter
Circuilt level metering
Water metering
Doorways sensors people, motion, open/close position

## Slide 9: Deployments Overview
Notes: We deployed contact reed sensors to detect the use of objects, including
-Appliances,
-Doors and cabnets
-And water fixtures

## Slide 10: Deployments Overview
Notes: actuators
Thermostat
As well as vent registers that wireless control airflow into each room individually
…
Each of our deployments was performed for a different experimental goal, and so not all of these sensors and actuators were deployed in all homes.

## Slide 11: Our Deployments
Deployment | # Homes | Weeks | Motion | Object Use | Door Heights | Wearable Tracking | Light Switch | Power (Plugs) | Power (Circuits) | Power (Mains) | Water Mains | Custom Thermostat | Active Register | Light/Temp Humidity
A | 11 | 1-2 | 25-30 | 12-20 | - | - | - | - | - | - | - | - | - | -
B | 1 | 1 | - | - | 12 | 12 | - | - | - | - | - | - | - | -
C | 3 | 3-4 | 15-25 | - | - | - | - | - | - | - | - | - | - | 12-25
D | 1 | 2 | 4 | - | - | - | - | 2 | - | - | - | - | - | -
E | 1 | 2 | 5 | - | - | - | - | - | 1 | - | - | - | - | -
F | 1 | 28 | 65 | 13 | 13 | 16 | 22 | - | - | 1 | 1 | 1 | 12 | 86
G | 1 | 44 | 54 | 7 | 31 | 14 | 22 | 8 | 37 | 1 | 1 | 1 | 12 | 29
H | 1 | 39 | 15 | 7 | 14 | - | 11 | 4 | - | 1 | 1 | - | - | -
I | 1 | 32 | 25 | 10 | 30 | - | 31 | 3 | 48 | 1 | 1 | - | - | 8
J | 1 | 25 | 14 | 5 | 17 | - | 7 | 2 | - | 1 | 1 | - | - | -
Notes: This table summarizes our main home deployments and the sensors installed in each.
Some of our early deployments lasted only a few weeks and contained primarily motion sensors, contact switches deployed on objects such as appliances, sinks, and light switches, and light/temp/humidity sensors.
Our later deployments included more complete sensor suites, although there was still variation among homes. The number and types of sensors deployed depends on the layout of the house and the types of fixtures and appliances. Furthermore, only one home was instrumented with heating and cooling actuation.

## Slide 12: Outline
Deployment Overview
Reliability and Failure Analysis
A Hitchhiker’s Guide
Notes: After collecting data from all of these deployments, we performed a post-facto analysis of sensor failures rates…. AND the root causes of these failures.

## Slide 13: Fault Analysis
…
Time
Sensors
Notes: Each deployment produces multiple data streams, each of which may sometimes have gaps that indicate data loss.
For each sensor type, we define a maximum gap length, beyond which the sensor is considered “down”. (click)
Then, we try to identify the root cause of this down time based on simultaneous sensor failures, such as this one (click).

## Slide 14: Failure Analysis
Notes: This diagram illustrates our system architecture, including a relay machine in each house multiple sensor sub systems connected through a USB hub and some connected directly through the internet router.
Based on this architecture, we define several types of failures. For example:
Battery failures cause down time in a single battery-powered device while plug disconnections cause down time in a single wall-powered device (click). In contrast, a power outage at the house causes simultaneous down time in all wall-powered sensors.
Failure of a wireless bridge of data collection script cause failure in an entire sensing sub-system (click)
Router failure causes down time in all sub-systems that directly connect to the internet (click)
And failure of the laptop in each houses causes down time in most sub-systems (Click)

## Slide 15: Fault Analysis
Power Outage
Time
Sensors
…
Sensor-Days – down time × number of sensors
Notes: We classify (click) all sensor down time in terms of a root cause by scanning through all data streams and looking for simultaneous failures in subsets of sensors with a common failure mode. (click)
We measure the effect of each root cause in terms of what we call “sensor days”: the amount of down time multiplied by the number of sensors.

## Slide 16: Fault Analysis
Reinstall
Hard drive failure
Sub-system failure
Plug disconnections
Notes: These graphs show the down time in four houses, classified by root cause in the period from Jan 1 to Aug 1, 2011. The figures have 2 dominating features.
First, the relay machine failed in one house, causing down time twice: first when we reinstalled the machine (click), and later for a longer period of time (click) when we diagnosed a hard drive failure, had a new hard drive shipped, and reconfigured the machine again.
Second, most data loss is caused by wireless bridge, software, or configuration errors shown in green that caused down time in entire subsystems (click). Not coincidentally, such failures were much more common after April 8, the deadline for this conference, when students no longer had immediate need for the data.
Looking closely at the blue area that indicates plug disconnections, we see a periodicity – approximately once per week – where many sensors are unplugged due to a cleaning crew and robotic vacuum. In fact, these plug disconnections caused more sensor down time than battery failure.

## Slide 17: Outline
Deployment Overview
Reliability and Failure Analysis
A Hitchhiker’s Guide
Notes: We use this quantitative analysis and other observations as a foundation for guidelines in our hitchhiker’s guide.

## Slide 18: Homes are Not a Power Panacea
  30-40 outlets per house
  Long wires
  2.3x more down time than batteries
More maintenance calls
Notes: One of the key differentiating feautures between sensing in homes and sensing outdoors is that homes have 120V AC power throughout the building. This certainly makes some sensing tasks easier, but also has its limitations: it does not simply make all power issues completely dissappear.
For example: we deployed over 300 sensors in one house that only had about 40 power outlets, so MOST sensors could not use the AC power.
Second, power is not available in doorways, on windows or many other locations where sensors must be placed, resulting in long wires running through the house. In one case, we had to run 250 feet of wire to power only 13 sensors.
Third, out analysis indicates that wall powered sensors have a 2.3 times more downtime. This is due to several reasons:
We found that people unplug sensors to use appliances such as hairdryer or a vacuum, particularly when the sensors occupy most available power outlets. In one home, we naively put sensors in all but 6 of the available power outlets. (click), even after using expansion packs
Long wires are often snagged or unlugged (click),
And wall-powered sensors are affected by power outages, which occur more frequently than we would have expected.
Finally, we also found that wall-powered sensors require far more maintenance calls than battery powered sensors. This is because battery powered sensors fail in a very predictable and correlated fashion, and all bat- teries can be changed at once in a single service call while wall-powered sensors fail independently. Fixing one disconnection does not prevent another one from happening tomorrow.

## Slide 19: Homes Have Poor Connectivity
Wireless connectivity
Power line communications
  Wires
  180bit/s
  5 min polling rate
Exploiting Home Automation Protocols
for Load Monitoring in Smart Buildings
Notes: We also found that connectivity in homes is worse than expected. Laptops and Wifi work well in homes, but sensors are often put in exceptional locations such as metal air ducts and metal junction boxes. They were also placed on or near concrete or masonry walls, heavy plaster, and metal appliances. Despite having hundreds of wireless devices in a small area, some of our sensors only had1 or 2 radio neighbors.
One alternative to wireless is power line communication: communicating with electrical signals on the AC power circuits. However, this is only a solution for sensor that can connect to an AC socket, which may be only a small fraction of the sensors in the house. Off the shelf powerline modems are effective but the cost \exceeds that of many sensors. As we saw in a paper at BuildSys on Monday, the low-cost solutions often used for sensing only support low data rates of about 180 bits per second and a 5 minute polling rate for the whole house.

## Slide 20: Homes are Hazardous Environments
Children
Mobile objects
Roomba
Guests and cleaning services
Notes: Just like large outdoor deployments, a small failure rate for a single sensor translates to larger rates when deploying tens or hundreds of sensors.
Home are not exposed to extreme weather or wild animals but through our experience, we have identified a number of unexpected causes of sensor failure in homes that lead to weekly and often daily system maintenance.
For example, sensors should always be child-proofed. (click) To you and I, this looks like a solid sensor design with reliable power, but to a 3 year old it looks like a nice addition to a lego tower. Before producing in quantity, a better design would have a through hole screw to hold the enclosure in the socket.
(click) Sensors should also be well secured for mobile objects such as brooms: (click) in one home, an electric vacuum periodically knocked many of our sensors out of their sockets.
(click) Sensors on sinks, light fixtures and appliances can easily be knocked off. You can’t count on people being careful with the sensors: many of our displaced sensors were knocked off by guests and cleaning services who were not familiar with our system.

## Slide 21: Homes are Remote Environments
Minimize installation time
  Scout
  Lab assembly and configuration
  Checklists
Notes: A main difference between residential sensing and outdoor deployments on islands or mountaintops is that homes are easily accessible for installation and continuous upkeep. However, we have found that this is not true when deploying in homes not owned by the researchers.
Volunteers make a personal time commitment for scientists to enter their home and de- ploy or maintain a system and Researcher need to use this time wisely:
-even a 10 minute visit requires an appointment.
-visits more than 4 hours are disruptive to the volunteer’s meal times and daily routine
-visits of a full day will be rare.
Therefore, it is critical to minimize on-site installation and maintenance time. If installing a single sensors takes only 10 minutes, installing 200 will take 4 days.
1. During the site visit, scout out the deployment position of every single sensor, take measure- ments, photographs, and make records on a floor plan.
-If wires are to be run, the path of the wires should be determined and exact measurements made so that the wires can be cut to the length before soldering. Check the location of pipes, the num- ber and locations of electrical panels, styles of faucet fixture, and the number of light switches, and if walls were plaster, concrete, or wallpapered.
-If accessing a crawl space, be sure somebody on site will be able to fit into it.
2. After the site visit, fully assemble and configure all sen- sors in the lab: give each node an ID and pre-determine its location. Print the locations on multiple floor plans so that multiple people can deploy the sensors in parallel. Cover LEDs before deployment; unlike programmable LEDs on experimental platforms
-Count the electrical sockets and bring expansion adapters or extension cables as neces- sary
-Count the tools needed for each installation and bring enough sets for parallel installation.
3. Bring flash lights, garbage bags, and a handheld vacuum cleaner for clean up afterward. Bring extra sensors to the site; some are sure to malfunction.

## Slide 22: Expect Limited User Participation
Button Tracking
Wearable Tracking
Self-reporting
Surveys
22
Notes: In homes, occupants can be a valuable source of information: who turned on the lights? What time did you eat dinner?
However, we have found that occupants participate to a limited extent, and the time they are willing to participate depends on the intensity of the task.
For example, users who tracked their own locations in the house by pushing a button in each room would participate for a few hours. People would tolerate a wearable tracking device for a few days, self-reporting on activities or appliance usage for a few weeks, or respond to telephone surveys for a few months.
Much like the energy in a sensor’s battery (click), user participation appears to come in finite quantities and can either be used intensely in short bursts or slowly over long periods.
It is not due to a lack of motivation, but rather that personal and family activities are a necessary part of life, even for co-investigators, and people can only tolerate so much interference due to participation in a residential sensing study.
.

## Slide 23: Aesthetics Matter in Homes
Disappear into the woodwork
Leave no trace
No LEDS at night
Noise
Notes: Aesthetic appeal is not typically a concern for wireless sensor network de- sign but is important in homes. Ugly systems are not viable in the long term because even in a scientist’s home, there are volunteers such as a spouse or children.
-Our early systems itroduced a lot of wires and exposed circuit boards (click) and due to push back from users, our later generations were designed to disappear into the woodwork (click).
-Sensors must look good not only during deployment, but also after the deployment is taken down. Double sided tape can peel paint, which is expensive and time consuming to repair. Putty doesn’t peel paint but is not necessarily reliable: in one house with hundreds of putty-mounted sensors, eventually lead to a cacophony of sensors crashing to the ground every 4-6 hours
- LEDs on electronic appliancessuch as televisions and clocks are a common annoyance for homeowners, but this becomes a “show stopper “ when scaling to hundreds of nodes. We calculate that our sensors introduced over 150 new LEDs into one home. These LEDs were not visible during the day-time deployment but residents complained that the house became a “circus” or a “laser light show” at night
- Finally, systems should be silent. For example, the occupants of one deployment disconnected all data collection devices when an uninterruptable power supply (UPS) began beeping incessantly at 5:30am due to a power outage. Several days of data were lost, and the system would actually have been brought back on-line much faster if the UPS had never been installed in the first place.

## Slide 24: Simplify the Architecture
Notes: In the residential domain, sensing and home automation are old industries with a wealth of commercial off the shelf (COTS) products, and in our deployments we used COTS devices whenever possible (Figure 1). These products reduce design time, but also have limitations.
Every new sensing task in a home typically requires a new COTS systems. However, each system introducing a new set of protocols and communication paths (click), bridges (click) , gateways (click), and software stacks (click). Deploying a dozen different COTS products in a single home is akin to maintaining a dozen sensor networks simultaneously, each with independent risks and failures, and we found that maintenance effort increases with the number of different sub-systems more than it does with the total number of sensors.
Despite the convenience of using COTS systems, we recommend building an integrated system on a single hardware platform to the extent possible in order to reduce the number of failure modes in the system.

## Slide 25: Similar Work
Infrastructure-based
  Neural Network House, Aware-Home, MavHome, PlaceLab
Infrastructure-less
  Tapia, Cook, Kasteren
Lessons Learned
  Edwards and Grinter – 7 challenges
  “Hitchhiker’s guides for WSN deployments”
Notes: Before our deployments, researchers have been deploying sensors in homes for decades.
Infrastructure based systems such as the Neural Network House required a retrofit of 5 miles of low-voltage wire to collect information or the Aware-Home which was custom built and contained a dedicated control room. There are also a number of infrastructure-less systems. (click) These systems use either a large number of sensors for a short period of time or a few sensors for a long period of time.
Many of the lessons discussed in this talk have undoubtedly been observed during these other home sensing projects, but These studies did not result in a comprehensive listing of these lessons learned or a distillation of guidelines from which future projects could benefit.
Some paper do produce guidelines but they are not about system issues.
They focus on social ramifications, the effect on home life, the challenges of ambiguous data.
A set of guidelines for outdoor sensor networks was summarized in a “Hitchhiker’s guide for WSN deployments”
In this paper, we compare and contrast the lessons from outdoor deployments when possible.

## Slide 26: Summary
AC Power is not abundant or reliable
Wireless connectivity is worse than expected
Unexpected environmental hazards
Houses are remote environments
User participation is limited
Aesthetics are important
COTS are a double-edged sword
Notes: In summary, we have distilled our experiences into 7 key points:
AC Power is not abundant or reliable
Wireless connectivity is worse than expected
Unexpected environmental hazards
Houses are remote environments
User participation is limited
Aesthetics are important
COTS are a double-edged sword

## Slide 27: Thank You
Any questions?

## Slide 28: Root Failures
Root Cause | House G | House H | House I | House J
Sensing sub-system | 4107 | 642 | 4757 | 274
Gateway Down | 5596 | 0 | 3 | 136
Plug Disconnected | 509 | 30 | 474 | 10
Battery Dead | 452 | 17 | 168 | 0
Wireless Link Loss | 410 | 0 | 122 | 1
Internet Down | 251 | 97 | 178 | 9
Power Outage | 21 | 0 | 87 | 2